## Slide 1: Vertikale referentie en getijreductie buiten Nederland
Martin.verlaan@deltares.nl

## Slide 2: Outline
Introduction
A global tide and surge model
LAT computations
Tidal corrections
MDT

## Slide 3
From regional to global
Operational storm-surge model in Netherlands DCSM-ZUNO

## Slide 4: Grid in DELFT3D-FM
Unstructured approach - step 1: grid thinning at high latitudes

## Slide 5: Grid in DELFT3D-FM
This DELFT3D-FM grid uses triangles and rectangles
for local grid refinement. Resolution is based on Courant number.
Unstructured approach - step 2: grid refinement in shallow areas

## Slide 7: Operational forecasts 4x per day
GLOSSIS uses FEWS environment

## Slide 8: A global LAT

## Slide 9: LAT worldwide
LAT version 2016

## Slide 10: Increased grid resolution
Deep water 50km 25km
Coast: 5km2.5km globally, 1.25km Europe
Smoothing at 2.5km resolution
Larger coverage of refinement at steep bathymetry (5km)

## Slide 11: IT dissipation- Results
BF dissipation (TW)– Literature ~2,5TW | IT dissipation (TW)– Literature ~1TW
2,47 | 1,17
Std ocean 10,3cm to 6,3cm
Std coastal observations 22,6cm to 16,4cm
Spatial pattern matches literature
Quantitative assessment made in resolution study (coming slides)

## Slide 12: Radiational tides
S1 atmospheric tide
S2 atmospheric tide
  Oceanic response to the atmospheric tides (“air tides”), resulting from solar radiation.
  Mainly pressure loading, wind stress considered negligible
  S1,S2,SS1,S1
  Harmonic analysis of surface pressure and wind stress maps from 7 years of ERA5 (0.25deg, 1hour)

## Slide 13: Radiational tides
Modelled tide [m] at Furuogrund (Baltic) without (upper) and with(bottom) radiational tides. Radiational seasonal signal is remarkable.
Tidal error change [%] relative to tidal range. Mediterranean and Baltic significantly improved

## Slide 14: The GTSMv3.0 performance – tides
Model | Type | deep ocean M2 | Coast M2
GTSMv3.0 | Non-assimilative | 3,5cm | 10,5cm
FES2012 | Assimilative(satellite) | -- | 4,5cm
Av. assimilative | Assimilative(satellite) | -- | 10,41cm
Best. Non-assimilative | Non-Assimilative | 5,63cm | 21.1cm
Comparison to state of the art tidal models from Stammer et al. (2014):

## Slide 15: Tide corrections

## Slide 16
Bathymetry from space : www.BASE-platform.com
SAR
Altimeter
Optical
Waterlevel
Crowd sourced
Notes: I would mention the complementary nature of the various data sources, eg different depth range.

## Slide 17: Coastline validation with satellite data
10% dry
90% dry
90% sealevel
10% sealevel
Low water
High water
Numerical
model
High-res
bathymetry
Satellite water
detection
Low waterline
High waterline

## Slide 18: Water occurrence to coastline

## Slide 19
Mean dynamic topography
Linking geoid to MSL

## Slide 20: Mean Dynamic Topography
m
Source: aviso
Satellite derived MDT

## Slide 21: GTSM MDT test
Simplified one layer model

## Slide 22
Questions?